## Slide 1: GOLD CODE

## Slide 2: Introduction to Gold Code
Gold Codes are a class of binary sequences used in spread spectrum communication systems.
They are generated by combining two maximum length sequences (m-sequences) using modulo-2 addition (XOR operation).
Gold codes are widely used in satellite navigation systems because of their:
Good cross-correlation properties
Large set of unique sequences
Predictable generation method

## Slide 3: GOLD CODE IN NavIC
NAVIC (Navigation with Indian Constellation) is India’s regional satellite navigation system developed by ISRO.
NAVIC uses Gold Codes for:
PRN (Pseudo Random Noise) code generation
Satellite identification
Signal separation in CDMA environment
Secure positioning services
Features of Gold Code in NAVIC:
Used in L5 and S-band signals
Supports Standard Positioning Service (SPS)

## Slide 4: GPS AND GOLD CODE
GPS uses Gold Codes for:
C/A Code (Coarse Acquisition Code)
PRN sequence generation
Satellite identification
Civilian positioning
Features of Gold Code in GPS:
Operates mainly in L1 band (1575.42 MHz)
1023-bit Gold code sequence
Repeats every 1 millisecond
Global coverage

## Slide 5: Working of Gold Code Generation
Working of Gold Code Generation
Gold code is generated by:
Two Linear Feedback Shift Registers (LFSRs)
Each LFSR generates an m-sequence
Output sequences are XORed
Different phase shifts create different PRN codes

## Slide 6: Advantages of Gold Codes
Excellent cross-correlation properties
Easy hardware implementation using LFSR
Large family of sequences
Robust against multipath interference
Suitable for CDMA systems

## Slide 7: Difference between